## Slide 1
specifies combinational logic (unclocked) always stmt.
should use “=“ (called “blocking” assignment) in comb. logic always statements. RHS just takes output from the previous equation.
“t” and “f” still declared as reg even though they’re used inside a comb. logic always stmt.
takes output of “t” from previous equation

## Slide 2
specifies clocked always statement with positive edge triggered flip-flops with negative reset.
“t” and “f” still declared as reg as they’re used inside an always statement (clocked always in this case)
RHS taken from FF output
this if part specifies how the registers should be initialized
this else part specifies how registers should be updated at each cycle.
all “outputs” (LHS) are stored in a register in a clocked always stmt. LHS specifies “new” value that will be stored after next clk tick.
should use “<=“ (called non-blocking assignment) instead of “=“, which means on the RHS, the value is the “current” value of the register.
LHS goes into FF

## Slide 3
any variable written to in an always stmt must be declared as a reg, incl. outputs
clocked always stmt
this if part specifies how the registers should be initialized
this else part specifies how registers should be updated at each cycle.
all “outputs” (LHS) are stored in a register in a clocked always stmt. LHS specifies “new” value that will be stored after next clk tick.
should use “<=“ instead of “=“, which means on the RHS, the value is the “current” value of the register.
all “outputs” (LHS) are stored in a register in a clocked always stmt.
If-then-else & case stmts translated as MUXes
Arithmetic operators (e.g. “+”) are replaced with library logic implementations.

## Slide 4
here, “y” is an “output” of this clocked always stmt, so it is stored in a register.
“<=“ should be used, which means on the RHS, “y” is the current value of the register, and on the LHS, “y <= …” is the new value that will be stored in the register on the next clk tick.
“x” is an external input to this clocked always stmt, so it’s not register.
1st always stmt
2nd always stmt
writes to “z” reg
reads from “z” reg
writes to “z” reg
reads from “z” reg
output from clocked always stmt is output of reg.

## Slide 5
specifies combinational logic (unclocked) always stmt.
should use “=“ in comb. logic always stmts. no reg. RHS just takes output from the previous eqn.
1st always stmt
2nd always stmt
takes most recent value of “z”
“z” still declared as a reg even though it’s used inside a comb. logic always stmt.

## Slide 6
always stmt
the 2 assign stmts
takes most recent value of “z”
note order of assign and always stmts does not matter.
“z” should be declared as a wire when used outside of an always stmt.

## Slide 8
logic always block
<<1
c
state
count
c
state
count
00
01
10
11
00
01
10
11
00
01
10
11
reset_n
clk
+
–
a
b
+1
myinc
0
0
s1
s2
s0
module rtl_example
clocked always block
+1
f
8
8
8
8
2
8
t
8